## Slide 1
Longitudinal dynamic in NICA Barrier Bucket RF System
at transition energy, including impedances in BLonD. Продольная динамики в ВЧ типа Barrier Bucket
при критической энергии с учётом импедансов в BLonD.
1
Докладчик: Колокольчиков С. 1 (kolokolchikov@inr.ru)
Со-авторы: Сеничев Ю.1, Аксентьев А. 1, Мельников А. 1,
Ладыгин В. 2, Сыресин Е. 2
1Институт Ядерных Исследований РАН, Москва, Россия
2Объединенный Институт Ядерных Исследований, Дубна, Россия.
Москва, 10 июля 2023 г.
10/07/2023
Москва, 2023 г.

## Slide 2
Abstract
2
10/07/2023
Москва, 2023 г.
В работе исследуется влияние импедансов пространственного заряда, а также ВЧ резонаторов на продольную динамику во время процедуры прохождения критической энергии скачком. Отличительной особенностью является применение ВЧ барьерного типа, результатом его использования является специфическое распределение пучка в фазовом пространстве, отличное от классического, образованного гармоническим ВЧ.
The paper investigates the influence of space charge impedances, as well as RF resonators, on longitudinal dynamics during the procedure of transition energy crossing with a jump. A distinctive feature is the use of Barrier Bucket RF, as a result a specific distribution of the beam in the phase space, different from the classical one formed by harmonic RF.

## Slide 3
TABLE OF CONTENTS
3
Longitudinal Dynamic
Transition Energy
Barrier Bucket
Impedances
BLonD
10/07/2023
Москва, 2023 г.

## Slide 4
Longitudinal Dynamic
4
10/07/2023
Москва, 2023 г.

## Slide 5
Equations of Longitudinal Motion
5
10/07/2023
Москва, 2023 г.
Slippage factor
– arrival Time drift
– Energy Kick
Synchronious Particle
Classical form
BLonD: https://blond.web.cern.ch/

## Slide 6
Transition Energy
6
10/07/2023
Москва, 2023 г.

## Slide 7
Transition
7
10/07/2023
Москва, 2023 г.
P. F. Derwent, Implementation of BLonD for Booster Simulations, Beams-doc # 8690, 2020

## Slide 8
Jump-scheme at NICA
8
10/07/2023
Москва, 2023 г.
– turns before jump
– turns at jump
–
– jump time
Here is a 5 different states of longitudinal
optics based on transition energy:
1) acceleration from injection energy with initial value;
2) smooth increase to peak;
3) jump;
4) smooth recovery till initial transition;
5) initial value till the experiment energy;
First defines 3) state based on the maximum available speed of transition shift and available transition size
Secondly, we can understand states 3 and 4, as they changed parallel to beam energy
Finally, states 3 and 5 also can be understand
1
2
5
4
3
3
2
4

## Slide 9
Momentum compaction factor at Transition
9
10/07/2023
Москва, 2023 г.

## Slide 10
Barrier Bucket
10
10/07/2023
Москва, 2023 г.

## Slide 11
Coasting Beam
11
10/07/2023
Москва, 2023 г.
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021

## Slide 12
Phase portraits of different BB
12
10/07/2023
Москва, 2023 г.
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021

## Slide 13
Barrier Bucket
13
10/07/2023
Москва, 2023 г.
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021

## Slide 14
Ferrite-loaded cavity
14
10/07/2023
Москва, 2023 г.
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021

## Slide 15
Ferrite-loaded cavity
15
10/07/2023
Москва, 2023 г.
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021
Ferrite-loaded cavity:
Fermilab Antiproton Debuncher
Fermilab Recycler Ring
GSI Experimental Storage Ring

## Slide 16
MA-loaded cavities
16
10/07/2023
Москва, 2023 г.
MA-loaded cavities:
Fermilab Main Injector
BNL Alternating Gradient Synchrotron (AGS),
KEK Digital Accelerator (DA)
KEK Proton Synchrotron (PS)
Facility for Antiproton and Ion Research (FAIR)
High Energy Storage Ring (HESR)
Schwerionensynchrotron
(SIS100)
Experimental Storage Ring (ESR)
COSY
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021
What is it
Difference

## Slide 17
The ESR BB system
17
10/07/2023
Москва, 2023 г.
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021

## Slide 18
Principle of stacking with BB
18
10/07/2023
Москва, 2023 г.
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021

## Slide 19
NICA Elements
19
10/07/2023
Москва, 2023 г.

## Slide 20
Barrier Bucket at NICA
20
10/07/2023
Москва, 2023 г.
A. Tribendis and others, Constraction and first test results of the barrier and harmonic RF systems for the NICA collider, IPAC2021, Campinas, SP, Brazil, doi:10.18429/JACoW-IPAC2021-MOPAB365

## Slide 21
Barrier Bucket at NICA
21
10/07/2023
Москва, 2023 г.
A.M. Malyshev and others, Barrier station RF1 of the NICA collider. Design features and influence on beam dynamics, RuPAC2021, Alushta, Russia, doi:10.18429/JACoW-RuPAC2021-WEPSC15

## Slide 22
Barrier Bucket Summarize
22
10/07/2023
Москва, 2023 г.

## Slide 23
Impedance
23
10/07/2023
Москва, 2023 г.

## Slide 24
Impedances
24
10/07/2023
Москва, 2023 г.
Laclare, J L (ESRF, Grenoble), Coasting beam longitudinal coherent instabilities, CAS - CERN Accelerator School : 5th General Accelerator Physics Course, pp.349-384, DOI: 10.5170/CERN-1994-001.349
Definition of Impedance:

## Slide 25
Space Charge Impedance
25
10/07/2023
Москва, 2023 г.

## Slide 26
Dispersion Relation
26
10/07/2023
Москва, 2023 г.
Laclare, J L (ESRF, Grenoble), Coasting beam longitudinal coherent instabilities, CAS - CERN Accelerator School : 5th General Accelerator Physics Course, pp.349-384, DOI: 10.5170/CERN-1994-001.349

## Slide 27
Vlasov’s Equation and Dispersion Relation
27
10/07/2023
Москва, 2023 г.
Laclare, J L (ESRF, Grenoble), Coasting beam longitudinal coherent instabilities, CAS - CERN Accelerator School : 5th General Accelerator Physics Course, pp.349-384, DOI: 10.5170/CERN-1994-001.349

## Slide 28
Impedances NICA
28
10/07/2023
Москва, 2023 г.
П.Р. Зенкевич, А.А. Коломиец
Электромагнитное моделирование
элементов структуры коллайдера NICA
Письма в ЭЧАЯ. 2020. Т. 17, № 4(229). С. 445–452

## Slide 29
NON-RF Impedances NICA
29
10/07/2023
Москва, 2023 г.
П.Р. Зенкевич, А.А. Коломиец
Электромагнитное моделирование
элементов структуры коллайдера NICA
Письма в ЭЧАЯ. 2020. Т. 17, № 4(229). С. 445–452

## Slide 30
RF Impedances NICA
30
10/07/2023
Москва, 2023 г.
П.Р. Зенкевич, А.А. Коломиец
Электромагнитное моделирование
элементов структуры коллайдера NICA
Письма в ЭЧАЯ. 2020. Т. 17, № 4(229). С. 445–452

## Slide 31
BB RF1 Impedances
31
10/07/2023
Москва, 2023 г.
Equivalent circuit of one ring (from the 1st to the 19th).
Last ring and accelerating gap.
System impedance calculated by equivalent circuit impedance
A.M. Malyshev and others, Barrier station RF1 of the NICA collider. Design features and influence on beam dynamics, RuPAC2021, Alushta, Russia, doi:10.18429/JACoW-RuPAC2021-WEPSC15

## Slide 32
BB RF1 Impedances
32
10/07/2023
Москва, 2023 г.
System impedance calculated by equivalent circuit impedance
A.M. Malyshev and others, Barrier station RF1 of the NICA collider. Design features and influence on beam dynamics, RuPAC2021, Alushta, Russia, doi:10.18429/JACoW-RuPAC2021-WEPSC15

## Slide 33
BLonD Beam Longitudinal Dynamic
33
10/07/2023
Москва, 2023 г.
BLonD: https://blond.web.cern.ch/

## Slide 34
BLonD. Scheme
34
10/07/2023
Москва, 2023 г.
Ring
Beam
Distribution
Profile
RF Station
Impedance source
Induce voltage
Tracker
Plot
P. F. Derwent, Implementation of BLonD for Booster Simulations, Beams-doc # 8690, 2020
BLonD Classes:

## Slide 35
BLonD. Ring
35
10/07/2023
Москва, 2023 г.
BLonD: https://blond.web.cern.ch/

## Slide 36
BLonD. Beam & Distribution
36
10/07/2023
Москва, 2023 г.
BLonD: https://blond.web.cern.ch/

## Slide 37
BLonD. RF Station
37
10/07/2023
Москва, 2023 г.
BLonD: https://blond.web.cern.ch/

## Slide 38
BLonD. Profile
38
10/07/2023
Москва, 2023 г.
BLonD: https://blond.web.cern.ch/

## Slide 39
BLonD. Tracker
39
10/07/2023
Москва, 2023 г.
BLonD: https://blond.web.cern.ch/

## Slide 40
BLonD. Resonators
40
10/07/2023
Москва, 2023 г.
Low frequency
High frequency
Example: RF1
BLonD: https://blond.web.cern.ch/

## Slide 41
BLonD. Inductive Impedance (SC) – Induced Voltage
41
10/07/2023
Москва, 2023 г.
BLonD: https://blond.web.cern.ch/

## Slide 42
BLonD. Users Impedance
42
10/07/2023
Москва, 2023 г.
BLonD: https://blond.web.cern.ch/

## Slide 43
Fourier Expansion
43
10/07/2023
Москва, 2023 г.
Mihaly Vadai, Beam Loss Reduction by Barrier Buckets
in the CERN Accelerator Complex, CERN, Geneva, 2021
Square signal
Sigma modulation
Fourier Expansion
RF Kick

## Slide 44
44
10/07/2023
Москва, 2023 г.

## Slide 45
Separatrix of BB
45
10/07/2023
Москва, 2023 г.
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021

## Slide 46
RF1 vs SC
46
10/07/2023
Москва, 2023 г.
BLonD: https://blond.web.cern.ch/

## Slide 47
Effect of High Order MCF
47
10/07/2023
Москва, 2023 г.
– smooth increase (2nd stage)
NO SC
BB RF
stationary
2
At 2nd stage
Taking into account
get a range of for different particles

## Slide 48
Space Charge & RF1 Resonant Impedance Effect at Transition Jump
48
10/07/2023
Москва, 2023 г.
Jump – (3d stage)
Only SC
No RF
change at a turn

## Slide 49
What’s Next
49
10/07/2023
Москва, 2023 г.
TO DO
Distribution match between 2-3 stages
Modeling 3-4 stages
Transition crossing with Harmonic RF (RF2?)
Another Impedance?
DONE
BLonD Modeling
High Order MCF
Resonant Impedance RF1
Space Charge Impedance
2

## Slide 50
References
50
10/07/2023
Москва, 2023 г.
Laclare, J L (ESRF, Grenoble), Coasting beam longitudinal coherent instabilities, CAS - CERN Accelerator School : 5th General Accelerator Physics Course, pp.349-384, DOI: 10.5170/CERN-1994-001.349
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021
Mihaly Vadai, Beam Loss Reduction by Barrier Buckets in the CERN Accelerator Complex, CERN, Geneva, 2021
П.Р. Зенкевич, А.А. Коломиец, Электромагнитное моделирование элементов структуры коллайдера NICA, Письма в ЭЧАЯ. 2020. Т. 17, № 4(229). С. 445–452
A. Tribendis and others, Constraction and first test results of the barrier and harmonic RF systems for the NICA collider, IPAC2021, Campinas, SP, Brazil, doi:10.18429/JACoW-IPAC2021-MOPAB365
A.M. Malyshev and others, Barrier station RF1 of the NICA collider. Design features and influence on beam dynamics, RuPAC2021, Alushta, Russia, doi:10.18429/JACoW-RuPAC2021-WEPSC15
P. F. Derwent, Implementation of BLonD for Booster Simulations, Beams-doc # 8690, 2020
BLonD: https://blond.web.cern.ch/